## Slide 1: FPGA Acceleration of DNA Sequence Mapping Team: DNA Mappers
Aditya Narayan Aastha ANAND G SIVA PERUMAL
SARTHAK JAGETIA ANAND SHIVALKAR

## Slide 2
Background and Motivation
High Level Diagram and Specifications
Functional Description of Blocks
Results and Analysis
Successes and Failures
Conclusion and Future Work

## Slide 3: Background
Substitution
Deletion
Insertion
Sequence Mapping
Central dogma of molecular biology

## Slide 4: DNA Sequence Mapping on FPGA
Short read mapping has traditionally been performed by software tools such as Bowtie, BWA , MAQ and BFAST running on a cluster of processors.
Huge Computational burden due to comparison of >1 billion short reads against a very long reference genome
Require 30-50 CPU days for complete mapping and alignment
Can be significantly accelerated by the use of FPGAs and GPUs
Olson, Corey B., et al. "Hardware acceleration of short read mapping." Field-Programmable Custom Computing Machines (FCCM), 2012 IEEE 20th Annual International Symposium on. IEEE, 2012.

## Slide 5: Scope and Motivation

## Slide 6
Background and Motivation
High Level Diagram and Specifications
Functional Description of Blocks
Results and Analysis
Successes and Failures
Conclusion and Future Work

## Slide 7: Initial High Level Block Diagram
.
Index Finder
FIFO
S-W
Score Tracker
DDR Memory (Index and Reference)
Short Read
Aligned Reads
…
Zedboard
Reference Lookup
S-W

## Slide 8: Final High Level Block Diagram
Indexing Block
Load Reference Sequence
FIFO
Smith Waterman PreProcessor
Systolic Array
Traceback
Smith Waterman Scoreboard
VGA Controller

## Slide 9
Background and Motivation
High Level Diagram and Specifications
Functional Description of Blocks
Results and Analysis
Successes and Failures
Conclusion and Future Work

## Slide 10: Indexing
Break down reference sequence into seeds (4 characters long) and store them in separate CAL tables
Compare seeds from the input short reads with the reference seeds
Identify all the indexes in the reference sequence where the short read can map with a high likelihood
TGTCCAGTATGCCTCCAGTAGATCGCATTCGAGAATCCGA
TGACCAGT
GCATAAGA
Index=0
Index=11
Index=24

## Slide 11: Verilog Code Implementation

## Slide 12: Smith Waterman Pre-Processor
Generate sequence 1 from the reference sequence using the index
Sequence 2 is the input short read
Store the sequences 1 and 2 in a FIFO until Smith Waterman is ready to compute :
  Smith Waterman takes n2 clock cycles to compute
  Indexing provides output every clock cycle until done

## Slide 13: Local Sequence Alignment – Smith Waterman Algorithm
Why Smith Waterman?
Commonly used for comparison of 2 strings
The fully gapped algorithm provides accurate scoring, even in the presence of indels
Search space is quadratic as opposed to exponential search space of other algorithms
Can be implemented efficiently using 2D systolic arrays

## Slide 14: Smith Waterman Implementation using Systolic Arrays
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
PE
A
T
G
C
A
T
G
C

## Slide 15: Smith Waterman Processing Element
Compute current score from
  Diagonal score
  Top score
  Left score
Find maximum of the 3 scores to assign to the current element
Combinational block executing every clock

## Slide 16: Traceback Element
To output the character of sequence 1 and sequence 2 at (i,j)
Diagonal value maximum : seq1 and seq2 match or SNP
Left value maximum : Deletion in seq2
Top value maximum : Insertion in seq2

## Slide 17: Verilog Implementation of Smith Waterman

## Slide 18: VGA Interfacing
Zedboard allows 12 bit colour output through VGA connector
So VGA_R, VGA_G, VGA_B all 4 bits each
Other pins used are Horizantal sync and Vertical sync

## Slide 19: I/O Interfacing & challenges
Serial Inputs from Smith Waterman block are displayed on the computer screen via VGA display cable
Dynamically displaying all the sequences from the previous module along with the index as shown.
Not easy because had to code for letters ‘A’, ‘G’, ‘C’, ‘T’ & ‘-’ .
So coding for 15 characters in one sequence and 2 sequences in total!
That’s 30 characters being displayed dynamically!
Displaying the numbers dynamically by coding for digits ‘0 – 9’ for 2 digit index given by the Smith Waterman algorithm
Too many if-else loop created too much constraints while synthesizing the code and it took nearly 30-40 mins for it to build.

## Slide 20: Verilog Implementation of VGA Controller

## Slide 21
Background and Motivation
High Level Diagram and Specifications
Functional Description of Blocks
Results and Analysis
Successes and Failures
Conclusion and Future Work

## Slide 23: Demo Movie 1 – Local Sequence Alignment
Seq1 – ACTGGTACTA
Seq2 – ACTGGACTGA
Objective – Find local sequence alignment of the 2 sequences

## Slide 24: Demo Movie 2
Ref Sequence: Length 50
TGTCCAGTATGCCTGACGTCGATCGCATTCGAGAATCCGAATAAAGTATT
Short Reads
TGGTAAAT
AGTCCGTA
CGTCGATC
Objective – Find the best match of the short reads in the reference sequence with substitution, insertions and deletions

## Slide 25
Background and Motivation
High Level Diagram and Specifications
Functional Description of Blocks
Results and Analysis
Successes and Failures
Conclusion and Future Work

## Slide 26: Successes
Performed Local Alignment of 2 sequences using Smith Waterman Algorithm
Implementation of CAL table for seeding the reference indexes
VGA Interfacing for output display
Timing Accurate Implementation of Smith Waterman Algorithm
Working Prototype for performing DNA Sequence Mapping – Not that efficient

## Slide 27: Failures
Integration of Indexing and Smith Waterman Block -> Timing and Routing Error
*Paste the routing congestion error*
Probably due to combinational implementation of Indexing

## Slide 28: Failures
Spent a lot of time on getting user input through UART (Putty)
Tried Parallel Smith Waterman Implementation, but couldn’t integrate with the top module
Long Sequences takes a long time to build, (place & route) -> might need some compression algorithm
Takes a long time for Place & Route (~45mins) -> Design not that efficient

## Slide 29: Work Allocation
High Level Block Diagram and Functional Specification – Everyone
Indexing Block – Siva, Anand
Smith Waterman Pre Processor – Anand
Smith Waterman Block – Aditya, Aastha
VGA Interfacing for I/O – Sarthak, Aastha, Aditya
Overall Integration – Aditya, Siva, Sarthak

## Slide 30
Background and Motivation
High Level Diagram and Specifications
Functional Description of Blocks
Results and Analysis
Successes and Failures
Conclusion and Future Work

## Slide 31: Future Work
Parallel Smith Waterman algorithm
Test with longer short reads and references
Store Reference sequence in DRAM and implement a DRAM controller
Burrows-Wheeler Transform for data compression to solve the short read mapping problem

## Slide 32: References
Olson, Corey B., et al. "Hardware acceleration of short read mapping." Field-Programmable Custom Computing Machines (FCCM), 2012 IEEE 20th Annual International Symposium on. IEEE, 2012.
Lopresti, Daniel P. "P-NAC: A systolic array for comparing nucleic acid sequences." Computer 20.7 (1987): 98-99.
Herbordt, Martin C., et al. "Single pass streaming BLAST on FPGAs." Parallel computing 33.10 (2007): 741-756.
https://en.wikipedia.org/wiki/Smith%E2%80%93Waterman_algorithm
Vermij, E. P. Genetic sequence alignment on a supercomputing platform. Diss. TU Delft, Delft University of Technology, 2011.
Special Thanks to Prof. Martin Herbordt and Prof. Wenchao Li for inputs